## Slide 1: Security Vulnerabilities in Bluetooth Low Energy
Rajib Dey
Debashri Roy
CAP 6135 Final Project
Educational Survey
Notes: Hello everybody, our topic for CAP 6135 project is security vulnerabilities in Bluetooth low energy. The bluetooth low energy is totally different from classic bluetooth. And security and vulnerably of BLE is now a well researched area for communication security. We would like to give some overall idea about BLE and then move forwards towards its vulnerabilities.

## Slide 2: Content
What is BLE?
Introduction to Security in BLE enabled devices
Related Works
Probable Security Flaws
Proposed Remedies
Future Directions
Conclusion
Notes: We will first discuss short introduction towards what Bluetooth Low Energy (BLE) is, explain it’s stack layer very shortly ,then explain how security features are implemented in existing specifications. Then we will go through the literature survey we did for this project. Next we will describe the probable security flaws in existing BLE technology, as per those surveyed papers, and our observations. We will also give some insight over the possible remedies for addressing those flaws. Next we will conclude this presentation.

## Slide 3: What is Bluetooth Low Enegy?
New modulation and link layer protocol for low power devices.
History of BLE
Differences with Classic Bluetooth:
    Incompatible with Classic Bluetooth
    PHY and Link Layer almost completely different
    High level protocols reused (L2CAP, ATT)
Notes: Bluetooth Low Energy (BLE) is now called Bluetooth Smart, and it is a part of Bluetooth 4 and was introduced in 2010. It is meant to be Designed for power-efficient and significantly smaller and cheaper. Devices such as Internet of Things. It supports low cost and easy implementation, which led BLE to be widely used among IoT devices and applications. It could be deployed in wearables, sensors, lightbulbs, medical devices, and many other smart-products. 48 billion IoT devices are expected to be in market and in our daily lives by 2021. Bluetooth Low Energy is predicted to be in nearly one-third of those devices.
Now a day, maximum laptops and smartphones have BLE in built in it. Bluetooth Smart Ready indicates a dual-mode device, typically a laptop or smartphone, whose hardware is compatible with both Classic and LE Bluetooth peripherals. Bluetooth Smart indicates an LE-only device, typically a battery-operated sensor, which requires either a SMART Ready or another SMART device in order to function. iPhone 4S was the first ever commercial device to include BLE.

## Slide 4: Protocol Stack in BLE
Notes: This is how the protocol stack in BLE looks like. A very brief description about all these layers are provided in the paper. Due to time constraints we will not present this here today. Just so you know, All the encryption, authentication happens in security manager part of the protocol. For the sake of this project we will focus on that.

## Slide 5: Communication in BLE Devices
Sends out advertisements ( by Advertisers)
The corresponding app looks for those advertisements ( by Scanner)
They find each other
Share Input-Output capabilities
Depending on that agree on a pairing process they choose one
Notes: What happens after you turn on a BLE device ? The advertiser, actually the BLE device, sends out advertisements. It provides a way for devices to broadcast their presence so that connection can be established between software and devices. It broadcasts data like the list of supported services, device name and TX power level. The app looks for advertisement and get paired based on some trivial security features. Once a connection is made the master, which may be the app device, informs BLE device of hopping sequence and when to wake up. All subsequent transactions are performed in the 37 data channels. Transactions can be encrypted. Both devices can go into deep sleep between transactions.

## Slide 6: Security in BLE
Five features for security
  Pairing
    Process for generating shared keys ( STK )
  Bonding
    Subsequent process of pairing where they store STK to form trust
  Encryption
    For message confidentiality
  Authentication
    Two device identify if they have the same keys
  Message Integrity
    To avoid attacker to forge data
Notes: After the devices find each other through advertisement they would go through some security procedures. Pairing would be the first one, where Short-term-Key would be generated. Then this STK is used to generate a few more security keys. Most important of all of those keys is the Long-term-key. After the STK is generated the communication is encrypted using the STK for the first time. After that the LTK is generated to encrypt all future communications.

## Slide 7: Pairing
Using keys to encrypt the communication
The keys can be used to encrypt future reconnections
Can also verify signed data, or perform random address resolution
3-phase for pairing
1.Pairing Feature Exchange I/O Capabilities
Depending on that choose method for phase 2
2.Short Term Key (STK) Generation (legacy pairing)
3.Transport Specific Key Distribution Long Term Key (LTK) used for LL encryption and authentication
Notes: If we just focus on pairing, it happens in 3 phases.
Generally speaking,
First phase determines the TK, seconds phase determines the STK and the 3rd phase determines the LTK.

## Slide 8: Pairing in BLE
How to determine the temporary key (TK)?
JustWorks™
Legacy, most common
Devices without display cannot implement other Its actually a key of zero, that’s why it just works...
6-digit PIN
In case the device has a display 1 million options (BF-able)
Out of band (OOB)
Does not share secret key over the 2.4 GHz band (used by protocol) Makes use of other mediums (e.g. NFC)
Once secret keys are exchanged, encrypts the channel Not common, barely used
Notes: The first phase can happen in one of these 3 method to determine the Temporary key.
It mainly depends upon the input/output capabilities of both devices. If one of the device does not have any input output capabilities then they would have to choose the “Just Works” method. Which is where we think Bluetooth Low-Energy is most vulnerable. Because in this case the TK is always zero.
In the last 2 phases STK and LTK is generated. To shorten this presentation we will skip that.

## Slide 9: Related Works
Uher et al., 2016. Simulated Denial of Sleep attack to drain BLE device's battery lifespan [1].
Lotfy et al., 2016. Security vulnerabilities for wearable devices [2].
Brauer et al., 2016. Proposed a jammer to show BLE vulnerabilities [3].
Cha et al., 2016. Used bluetooth MAC address of BLE devices to increase the security of pairing process [4].
Ortiz-Yepes, 2015. Presented a set of cryptographic protocols to minimize the BLE vulnerabilities [5].
Qu et al., 2016. Designed an extension for security during networking of BLE enabled devices [6].
Notes: We did literature survey on several published papers from 2016 to state of the art. We amazingly found that most of the work tried to address the security issues by providing some light-weighted cryptographic algorithms or proposing new application layer protocol, however none implemented in modern off-the-shelf BLE devices. As our project’s purpose is to provide an educational survey, so we are giving a deeper details of the studied papers, here:
In the first one, the authors introduced with a special type of attack for BLE devices, called Denial of Sleep attack. BLE devices work with two main status: active and sleep. Devices enters into sleep mode when it is inactive for a certain amount of time, which is generally vender and device type specific. However, this special type of attack is build on leveraging this concept. The authors have presented thorough analysis on how devastating this attack could be to BLE sensing network, by giving an example implementation. Denial of Sleep attack poises threat to BLE device's lifespan by several orders of magnitude, resulting the network largely unusable. Ultimately, the authors have modified different BLE protocols to allow a malicious actor to rapidly drain battery lifetime of a targeted BLE sensing node. The authors have given corresponding simulation results, including power analysis, in the paper.
In second paper, the authors have mainly focused on how the products live up to the security constraints for users' privacy. Three different types of Bluetooth LE pairing strategies were discussed here at a packet and protocol level. In the paper, the authors have examined three commercial wearables, where each use the different pairing processes. First, Jawbone UP (Jawbone), uses just works. Second, Pebble Steel smart watch (Pebble), uses numerical comparison. Lastly, the Fitbit Charge HR (Fitbit) uses passkey entry. The authors also stated specific methodology to test each of the devices and their associated pairing process, during their experimentation. The experimental results have shown that presumably secure pairing strategies have convincing security vulnerabilities that affect all of the devices considered.
In third paper, the authors have presented the concept of selective jammer for BLE devices. The proposed jammer can be programmed for BLE advertising in such a manner that only specific beacons, e.g. those with a particular MAC address, can be jammed. This exhibits a potential security loophole in BLE architecture. The proposed jammer leverages the technique that BLE beacons are sent on different advertisement channels. The jammer scans all advertisement channels in order to get estimate which channels are actually being used by the beacon sources, by its discovery component. Later those channels are attacked by the jammer to be interfered. The mentioned jammer transmits short jamming signal only on the attacked channel being used by the beacon frame, making it hard to detect, and energy efficient. The authors have also prototypically implemented the proposed jammer using low-cost, off-the-shelf and small-sized hardware. They were successful in showing the feasibility and efficiency of those jammers through experimental analysis.
In fourth mentioned paper, the authors have show how bluetooth MAC address of BLE devices could be used to increase the security of pairing processes. As mentioned earlier, pairing process of any BLE devices poises maximum vulnerability. The authors claimed that assignment of random MAC address in most of modern generation BLE enabled devices can make those susceptible to higher security risk. However, the idea behind random MAC address for BLE enabled devices were to provide better security by barring the easiness of tracking those devices. The authors bolstered their claim by a study using a smart vehicle from a major Taiwanese brand. The authors have also provided some generalized security requirements for the example scenario.
In fifth paper, the author presented a set of cryptographic protocols to minimize the BLE vulnerabilities. The author identified that security mechanisms provided in BLE specification sometime fails to provide suitable protection during accessing or modifying sensitive sensor parameters, or exchanging messages. He proposed Bluetooth Low Energy Application Layer Security Add-on (BALSA). BALSA specified set of cryptographic protocols, a BLE service and a guideline about usage architecture targeting to provide a suitable level of security. He also defined and analyzed these components and demonstrated the feasibility and benefits of BALSA by presenting an experiment with 4 BLE enabled smartphones.
In last paper studied, the authors have designed an extension during networking of BLE enabled devices. The authors have first extended a calculation formula for Authentication to accurately assess the vulnerability of BLE enabled IoT devices. The Authentication variable was first used by the National Infrastructure Advisory Council to determine conventional base score equations of the Common Vulnerability Scoring System (CVSS) v2. Later they have proved the superiority of their proposed extension over the current CVSS v2 base score by an experiment on network based shopping cart IoT system.

## Slide 10: Probable Security flaws
Use of “Just Works” to generate TK
Not implementing any kind of encryption or poor implementation
Sending sensitive information without encryption
Using easy-to-guess passwords
Flaws in Key-exchange process makes it vulnerable to active/passive eavesdropping
Lack of OTA capabilities
Poor Random number generator
Optimizing advertisement interval
Notes: After some detailed research, we found some vulnerabilities in BLE Security, they are enlisted here. We have found out these flaws, how they can be exploited, and how to avoid them, throughout the course of our extensive research.
Use of “Just Works” to generate TK for devices with limited I/O Capabilities.
Not using Out of band ( OOB ) medium to generate the TK.
Sometimes some vendors do not bother to implement any kind of encryption tor implement it poorly to cut cost and quicken the production time.
Sending sensitive information through plaintext without encryption.
Using Password based authentication which is just waiting to be brute-forced, if most common passwords like 123456 is not being used that s. But unfortunately most BLE devices uses such easy passwords.
Flaws in the Key-exchange process which can be vulnerable to active/passive eavesdropping.
Most if not all BLE capable peripheral devices lack OTA (Over-the-Air Programming) capabilities. So, if any vulnerabilities were found and it is fairly easy
to fix it, these devices will remain vulnerable.
-The process to randomize a number is not that random and can be reverse engineered if it is not implemented well.
-To save energy, BLE devices optimize the advertisement interval. They try to send advertisement packets in large intervals. If the attacker sends out his/her own advertisement packet at higher frequency then that can lead to jamming of the BLE device. This can also lead to Denial of Service (DoS) attacks

## Slide 11: Possible Countermeasures
Use encryption and authentication for advertisement
Use OOB or ECDH to exchange keys
Have a physical button on the device to authenticate
Use sequence number to prevent replay attack
Implement existing protocol in a robust manner
Implement OTA capabilities
Notes: Here are some possible countermeasures we can take to overcome the security flaws in BLE enabled devices.
- First, we need to use encryption and authentication while advertising broadcast values. Values in the advertisement Should not remain the same, they change the values which can only be decoded from the predefined devices. Services should not solely be performed using advertisement only (like heart-rate monitor broadcasting hear rates in advertisement packets). All services should go through proper encryption and authentication
Use of OOB or ECDH ( Whichever is applicable) would be one of the best ways to secure the key exchange against any kind of attacker.
If there is a predefined action that needs to be done by the user on the device to authenticate ownership then attackers can not discard old keys and force the device to generate new one, which the attacker can get to.
To prevent any replay attack a sequence number should be used for each message being sent and received. So that if a attacker resends old messages to perform a task desired by the attacker, the sequence number would not match and the message would be discarded.
Always implement existing encryption protocol in a robust manner. Encrypt all useful data being sent to prevent passive monitoring data Leaks.
Implement OTA capabilities into each device. This includes leaving enough room in the device memory so that codes can be updated easily if there is any vulnerabilities found. Without an OTA capable device we would have no other option than to just through away the device to avoid being hacked.

## Slide 12: Conclusion
BLE lags behind for providing a robust security mechanism with trade-off for cost.
Presented a comprehensive study to help users to understand how crucially security measures should be taken care of for BLE enabled devices.
Modern market of BLE is ignorant about security implementation.
Given insights about Security flaws and possible solutions.
Notes: We surprisingly found that Bluetooth Low Energy, being mostly different from standard Bluetooth architecture, still lags behind, in case of providing a robust security mechanism, as a trade-off for cost. However those vulnerabilities could be fatal and poise severe threat to the users privacy.
Our comprehensive study will help the users to understand how crucially the BLE enabled devices need to give extra attention towards implementing security features, and how modern market is mostly ignorant about that.
We have also presented our insights about some possible security flaws and possible solutions.

## Slide 13: References
J. Uher, R. G. Mennecke and B. S. Farroha, "Denial of Sleep attacks in Bluetooth Low Energy wireless sensor networks," MILCOM 2016 - 2016 IEEE Military Communications Conference, Baltimore, MD, 2016, pp. 1231-1236.
K. Lotfy and M. L. Hale, "Assessing Pairing and Data Exchange Mechanism Security in the Wearable Internet of Things," 2016 IEEE International Conference on Mobile Services (MS), San Francisco, CA, 2016, pp. 25-32.
S. Brauer, A. Zubow, S. Zehl, M. Roshandel and S. Mashhadi-Sohi, On practical selective jamming of Bluetooth Low Energy advertising. 2016 IEEE Conference on Standards for Communications and Networking (CSCN), Berlin, 2016, pp. 1-6.
S. C. Cha, C. Y. Dai and J. F. Chen, "Is there a tradeoff between privacy and security in BLE-based IoT applications: Using a smart vehicle of a major Taiwanese brand as example," 2016 IEEE 5th Global Conference on Consumer Electronics, Kyoto, 2016, pp. 1-4.
D. A. Ortiz-Yepes, "BALSA: Bluetooth Low Energy Application Layer Security Add-on," 2015 International Workshop on Secure Internet of Things (SIoT), Vienna, 2015, pp. 15-24.
Y. Qu and P. Chan, "Assessing Vulnerabilities in Bluetooth Low Energy (BLE) Wireless Network Based IoT Systems," 2016 IEEE 2nd International Conference on Big Data Security on Cloud (BigDataSecurity), New York, NY, 2016, pp. 42-48.
Notes: Here are the listed research papers we studied for our project.

## Slide 14
Thank You!
Notes: We want to thank the audience for their time and interest.