## Slide 1
Secure Spectrum Sensor Using MQTT Protocol
Group #4
Members: Rajib Dey, Debashri Roy, Cody Baker, Kennedy Vrutaal

## Slide 2
Content
What is a spectrum Sensor ?
Why Spectrum Sensor IoT?
Where is the Security?
Overview of the Project
Project Flowgraph
Collected Data
Demo Video of the Project
Conclusion & Future work
Q & A

## Slide 3
What is a spectrum Sensor ?
Can “Sense” a range of Spectrum Our sensor R820T SDR by NooElec has a range of 25MHz to 1750MHz
Commercially available from least expensive to more expensive ($15-$4000+) Our sensor cost about $19 per piece

## Slide 4
Why spectrum sensor IoT?
Controlling is important for commercial and academic use
Can control frequency-range from other devices over Internet
Useful in Dynamic Spectrum Access (DSA) implementation and other research work on wireless communications
Useful to store data in Spectrum Database

## Slide 5
Where is the security?
Implemented MQTT for collecting data over the Internet
Data consists of:
  RSSI (Received Signal Strength Indicator) values in dB at particular frequency
  GPS location ( Latitude and Longitude value)
  Date time
Implemented certificate based TLS communication for MQTT
Used a TCP socket connection to control frequency range from different device
Implemented certificate based TLS communication for TCP socket connection

## Slide 6
Overview of the Project
Sensor
RaspberryPi
Laptop/PC
GPS Module
Server
MQTT Protocol using Certificate based Mutual Authentication
Controller
TCP protocol using Certificate based Mutual Authentication
Preferably over strong Wi-Fi Signal

## Slide 7
Project Overview: Equipment
Raspberry Pi
GPS Module
  Adafruit Ultimate GPS Breakout MTK3339
Spectrum Sensor
  NooElec R820T Mini SDR
Controller Device
  Laptop
Data collection/Server Device
  Laptop

## Slide 8
Project Flowgraph
Connect the Pi to Wi-Fi
Connect the Sensor to the USB port
Connect the GPS module
Install Necessary software on the Pi
Run the python program
Connect the laptop to Internet or the same Network
Have the server and Controller Up and Running
Run the python controller program to control sensor
Run the python program to collect data
Data Collection
Data is collected and saved in the excel file
An Optional Graph is generated inside the Excel file
Use data
For future Research purposes
Eliminating Dead zone etc.

## Slide 9: Collected Data
Day 1: Set 1
  Frequency Range: 55MHz-65MHz
  Outdoor: UCF Campus
  Duration: 1 Hr
  Date: 21st Nov, 2017
Chart: Frequency versus RSSI Plot

## Slide 10: Collected Data
Day 1: Set 2
  Frequency Range: 55MHz-65MHz
  Outdoor: UCF Campus
  Duration: 1 Hr
  Date: 21st Nov, 2017
Chart: Frequency versus RSSI Plot

## Slide 11: Collected Data
Day 2:
  Frequency Range: Variable
  Indoor: HEC 313
  Duration: 24 Hrs
  Date: 25th-26th Nov, 2017
Chart: Frequency versus RSSI Plot

## Slide 12: Conclusion & Future Work
Conclusion
  Implemented Secure Spectrum Sensor using MQTT protocol
  Controlling the Spectrum Sensor over secure TCP Connection
  Collected data and saved it for later use
Future Work
  Use USRP B/N series for wider range of Spectrum Sensing
  Implementation of Spectrum database for dynamic data collection and use

## Slide 13: Q & A
Questions?